Oxide Growth Physics:

        Given the main result of the Deal-Grove model of thermal oxidation,

, we can directly use the thin oxide approximation for the 4nm thin oxide of the 180nm technology node. Because the oxide is thin, the oxidizing agent, in this case o2 in a dry ambient, decreases approximately linearly between the ambient/oxide interface and the oxide/silicon interface. Ignoring the parabolic term, the growth time becomes

Furthermore, xi will be 0 since this is only a simulation run and there is no initial oxide grows due to any wrong preservation of the wafer. The growth time finally becomes t = Ax0 / B.

 But B/A = C exp(-E/kT), where E is the activation energy of the oxidizing mechanism used. For dry O2 , C = 6.23e6 um hr-1 and E=2eV, which gives us B/A = 0.2651 nm/min. This tells us that to grow 4nm of oxide we need t=15 minutes, which is not the actual time we needed on our simulation.

     According to Wikipedia, the Deal-Grove model overestimates the needed growth time for oxides thinner than about 25nm for reasons that are not yet theoretically well understood. So for oxides with thickness below the 25nm threshold more sophisticated models must be used.